## Slide 1: EMEA SAN Environment
Zbigniew Klos, EMEA SAN L3

## Slide 2: EMEA DC’s with SAN equipment
RDC (Riverdale - primary London site)
CGC (Canary Wharf – small London site)
FDC (Frankfurt – CoB site for most apps except Rainbow)
Welle (small Frankfurt DC)
Colt (Zurich)
Interxion (Zurich)

## Slide 3: EMEA SAN Arrays
Non-replicated VMAX arrays: all sites (Swiss sites and Welle – only one array per site)
Replicated VMAX arrays: RDC,FDC,CGC
VSP arrays: RDC, FDC (USP-V’s – decommed)
HUSVM arrays (bronze): RDC,FDC,CGC (1 per site)
XIV arrays: RDC,FDC (2 per site)

## Slide 4: EMEA SAN Arrays – cont’d
VNX7500: RDC, FDC (2 per site; Exchange 2010 only)
CX4+AX4: RDC, FDC (Exchange 2007 only)

## Slide 5: EMEA VMAX Replication
Most VMAX arrays are unidirectional
Most apps replicate RDC->FDC
Prod site for Rainbow is FDC hence Rainbows arrays replicate FDC->RDC
Some apps replicate RDC->CGC
No HDS replicated arrays anymore

## Slide 6: EMEA SAN Fabrics - disk
EMEA disk fabrics are called Ruby and Jade (equivalent to A and B in the new naming scheme)
RDC Ruby/Jade
CGC Ruby/Jade
FDC Ruby/Jade
Colt Ruby/Jade (1 switch/fabric)
Interxion Ruby/Jade (1 switch/fabric)

## Slide 7: EMEA SAN Fabrics – disk – cont’d
Welle has no dedicated Ruby/Jade fabrics; uses VSANs on Silver/Gold switches
There are islands created for specific purposes via VSANs (e.g. Exchnage 2010 has VSANs on RDC/FDC Ruby/Jade fabrics)

## Slide 8: EMEA tape fabrics
EMEA tape fabrics are called Cat and Dog
RDC Cat/Dog overlap partially with RDC Ruby/Jade
CGC Cat/Dog connected via DWDM with RDC Cat/Dog
Hence RDC Ruby+RDC Cat+CGC Cat form one physical fabric
Same situtaion with RDC/CGC Jade/Dog
CGC Cat/Dog switches being decommed

## Slide 9: EMEA tape fabrics – cont’d
Similar situation in FDC
FDC Cat overlaps with FDC Ruby and is connected via DWDM with Welle Cat
Same situation with FDC Jade/Dog
Colt DC has two small Cat/Dog fabrics (9124)
No tape fabrics in Interxion

## Slide 10: EMEA Replication fabrics
Replication fabrics are called Silver and Gold
Each fabric spans 4 DCs (RDC+CGC+FDC+Welle)
One switch per fabric per site
No replication fabrics in Switzerland

## Slide 11: Switch vendors
Most fabrics built on EMC switches (both legacy 95xx and new 9710/9148S)
CGC Ruby/Jade fabircs built purely on HDS switches (legacy 9513 + new 9710/9148)
Some HDS 9513 switches are used in EMC RDC/FDC Ruby/Jade fabrics (hence these are mixed vendor fabrics)
Some 9148’s (non-S) were purchased from HDS – used in CGC Ruby/Jade and will be used in new Exchange 2010 dedicated fabrics
Some 9148’s (non-S) from EMC used in legacy RDC/FDC Ruby/Jade fabircs

## Slide 12: Mgmt servers - VMAX
RDC Linux hosts: rgcctisanla01p/rgcctisanla02p
RDC Linux hosts (MSC only): rgcctisanla04p/ rgcctisanla05p
CGC Linux hosts: cgcctisanla01p/cgcctisanla02p
FDC Linux hosts: fgcctisanla01p/fgcctisanla02p
FDC Linux hosts (MSC only): fgcctisanla04p/ fgcctisanla05p

## Slide 13: Mgmt servers – VMAX – cont’d
Welle Solaris hosts: welsan-mgt1/welsan-mgt2
Colt Linux hosts: zhctipgs05/zhctipgs06
Interxion Linux hosts: zhcticgs05/zhcticgs06

## Slide 14: DCNM servers (VM’s)
rdcctidcnva01p -> RDC Ruby/Jade (includes overlapping RDC Cat/Dog and CGC Cat/Dog fabrics)
rdcctidcnva02p -> CGC Ruby/Jade + EMEA Silver/Gold
fdcctidcnva01p -> FDC Ruby/Jade (includes overlapping FDC Cat/Dog and Welle Cat/Dog fabrics)
fdcctidcnva02p -> Colt Ruby/Jade + Colt Cat/Dog + Interxion Ruby/Jade

## Slide 15: RADIUS servers (same as DCNM)
rdcctidcnva01p -> primary RADIUS for all RDC and CGC switches
rdcctidcnva02p -> secondary RADIUS for all RDC and CGC switches
fdcctidcnva01p -> primary RADIUS for all FDC, Welle and Swiss switches
fdcctidcnva02p -> secondary RADIUS for all FDC, Welle and Swiss switches

## Slide 16: HTM servers (same as DCNM)
rdcctidcnva01p -> primary instance for HDS RDC 9513’s (in Ruby/Jade) and HDS CGC 9513/9710/9148’s (entire Ruby/Jade)
rdcctidcnva02p -> standby instance for HDS RDC 9513’s (in Ruby/Jade) and HDS CGC 9513/9710/9148’s (entire Ruby/Jade)
fdcctidcnva01p -> primary instance for HDS FDC 9513’s (in Ruby/Jade)
fdcctidcnva02p -> standby instance for HDS FDC 9513’s (in Ruby/Jade)

## Slide 17: HCS 8 servers (VMs)
ldnctisvhm002 -> all RDC and CGC VSP+HUSVM arrays
ffctisvhm002dr -> all FDC VSP+HUSVM arrays
Linux components running on Linux VMAX hosts (e.g. rgcctisanla01p/rgcctisanla02p for RDC etc.)

## Slide 18: U4V servers (VMs)
U4V VMs talking oo arrays via SYMAPI server on Linux management hosts
ldnctispa001/ldnctispa002 -> RDC arrays (divided 50/50 between the two instances)
fftctispa001/fftctispa002 -> FDC arrays (divided 50/50 between the two instances)
No U4V for CGC, Welle and Swiss DCs

## Slide 19: ESRS gateways (VMs)
3 VMs in RDC (ldnctisvea004/ldnctisvea005/ ldnctisvea006)
3 VMs in FDC (ffctisvea004/ffctisvea005/ ffctisvea006)
Gateways with same number create a HA pair
Devices spread across those 3 HA pairs

## Slide 20: XiV and VNX management hosts (VMs)
rgcctisanla03p -> Linux XCLI+XRSC proxy for RDC/FDC XiV arrays; ISIS for RDC arrays only
fgcctisanla03p -> Linux XCLI+XRSC proxy for RDC/FDC XiV arrays; ISIS for FDC arrays only
ldnctisanav001/ldnctisanav002/ffctisanav001/ffctisanav002 – Windows XCLI/XGUI/XTOP for RDC/FDC XiV’s
These 4 Windows VMs also have Unisphere for VNX installed to manage all EMEA VNX/CX4/AX4 arrays

## Slide 21: RDP to Windows hosts
EMEA has never purchased terminal server licenses for Windows VMs
Hence only 2 concurrent user sessions via RDP per VM